## Slide 1: Predicting Strength of High-Performance Concrete
Adam Philips
Springboard Data Science Capstone Project

## Slide 2: The Problem
High-performance concrete (HPC) is a complex engineered material for construction applications
HPC contains a mixture of conventional concrete materials (water, cement, fine and coarse aggregate) and several supplemental ingredients (blast furnace slag, fly ash, superplasticizer)
Due to its compositional complexity, the properties of HPC are difficult to model
What are the most important factors influencing the strength of HPC?
Can we predict the compressive strength of a concrete sample by its composition and age?

## Slide 3: The Data
1030 entries  996 after deduplication
8 Features:
  Cement, Blast Furnace Slag, Fly Ash, Water, Superplasticizer, Coarse Aggregate, Fine Aggregate (kg/m3)
  Age (days)
Target variable: Compressive Strength (MPa)
Supervised learning, regression problem
https://archive.ics.uci.edu/dataset/165/concrete+compressive+strength

## Slide 4: Which Features are most Important?

## Slide 5: Exploring the Data

## Slide 6: Modeling
Preprocessing:
Normalize the data row-wise. I.e. mixture components as fractions of the whole
For ‘Age’ feature, use min-max scaling on the column
Split data into training and testing sets (80/20 split)
The chosen models:
Linear regression
Random Forest
Gradient Boost
Hyperparameter Tuning and evaluation metrics:
5-fold cross-validation
R2
MAE
RMSE

## Slide 7: Comparing the Models
Model | R2 | MAE | RMSE
Linear Regression | 0.66 | 7.42 | 9.25
Random Forest | 0.92 | 3.32 | 4.52
Gradient Boost | 0.93 | 2.81 | 4.26
Test set:

## Slide 8: Gradient Boost Predictions

## Slide 9: Final Analysis
The optimize module from the scipy library was used to determine a set of feature variables that maximize the target variable (compressive strength) according to the fitted GB model.

## Slide 10: Final Analysis

## Slide 11: Conclusions
Of the ML models investigated, Gradient boost performed the best in predicting the compressive strength
GB model is fast and robust against missing values and outliers. It delivers state-of-the-art results at low cost.
A more robust study of concrete effectiveness would require analysis of other properties, i.e tensile strength, durability, thermal resistance.